## Slide 1: Advanced Sewage Treatment Plant
A cutting-edge, chemical-free, low-maintenance wastewater system
Electrocoagulation | Ultrafiltration | Fractionation Filter | Advanced Oxidation
Oceanides Malabanan Services

## Slide 2: Overview
A quick look at our Advanced STP
Chemical-free, low-maintenance design
Handles both domestic and industrial wastewater
Compliant with environmental regulations (DENR DAO 2016-08 and 2021-19)
Process begins at the effluent tank discharge, where a submersible pump starts the flow through every treatment stage
Four Treatment Stages
1
Electrocoagulation
2
Ultrafiltration (UF)
3
Fractionation filter
4
Advanced oxidation

## Slide 3: Treatment Process Flow
From effluent tank to safe discharge
Effluent tank + submersible pump
Electro-coagulation reactor
Ultra-filtration (UF)
Fractionation filter
Advanced oxidation O3 + UV
Safe discharge
Every drop of water goes through meticulous, multi-stage purification.
Removes suspended solids, organics, bacteria, viruses and microbial contamination,
so effluent meets regulatory standards and is ready for responsible discharge.

## Slide 4: Stage 1: Electrocoagulation Reactor
Treating wastewater with electrical current
Electroflotation: electrical current treats and flocculates contaminants without adding coagulants such as alum or polymers
Pairs of metal rods: two anodes and two cathodes, using the principles of electrochemistry
The anode is oxidized while water is reduced, improving overall treatment
Particulates are neutralized, forming hydroxide complexes that create flocs
Flocs settle at the bottom of the tank and are removed through filtration
+
Anode
-
Cathode
+
Anode
-
Cathode
Flocs collect at the bottom
Illustration: simplified electrocoagulation cell

## Slide 5: Electrocoagulation: What It Removes
Optimizing performance
Pollutants removed
Turbidity
BOD and COD
Oil and grease
Surfactants
Nitrates
Phosphates
Optimal removal depends on electrode material, pH and current density
Adept at removing small particles: direct current sets them in motion
Reduces residue, minimizing waste production in the treatment system

## Slide 6: Stage 2: Ultrafiltration (UF)
Pressure-driven glass media filter separation
Pressure-driven glass media filter separation process
Eliminates suspended particulate matter from water
Targets dissolved compounds of high molecular weight, such as organics and total dissolved solids
Efficiently removes bacteria and most viruses
Especially well suited for tertiary treatment of sewage
Raw water in
Glass media
Clean water out

## Slide 7: Stage 3: Fractionation Filter
Preparing the water for final treatment
Maintains high removal efficiency with 0.1 micron pore size
Captures suspended particles, bacteria and viruses
Ensures a thorough purification process
Prepares the water for the final treatment stage
Particles, bacteria, viruses
Membrane: 0.1 micron pores
Purified water

## Slide 8: Stage 4: Advanced Oxidation + UV
Ozone gas combined with ultraviolet disinfection
Advanced oxidation with ozone gas removes microbial contamination
Ultraviolet disinfection is an effective final barrier, a crucial part of tertiary wastewater treatment
Microbes exposed to UV light have their DNA destroyed
Disinfects the water and ensures harmful microbes are eradicated
UV lamp
O3
O3
O3
O3
O3
O3
O3
O3
O3
Ozone (O3) + UV in water

## Slide 9: Conclusion
Ready for responsible discharge
Effluent water surpasses regulatory standards
Comprehensive process combining cutting-edge technologies: electrocoagulation, ultrafiltration, fractionation filter and advanced oxidation
Every drop of water undergoes meticulous purification
Thank you